## Slide 1
PHL / NEU 251 · SESSION 4
The instruments:
measuring minds
recorded signal
METHOD
ANALYSIS
WARRANT
1

## Slide 2
Neural events become evidence through a chain of choices
METHOD
ANALYSIS
WARRANT
2
1
EVENT OR INTERVENTION
Neural activity changes, or a researcher changes the system.
2
SIGNAL OR OUTCOME
A physical signal or behavioral outcome becomes observable.
3
RECORDED DATA
The instrument samples, filters, and stores measurements.
4
ANALYZED RESULT
A contrast, model, or classifier summarizes the data.
5
CLAIM
The result is interpreted as evidence about mind or behavior.
Each step introduces assumptions.

## Slide 3
We’ll deal with four kinds of evidence
METHOD
ANALYSIS
WARRANT
3
OBSERVE OR RECORD
Existing lesions, structural MRI, DTI, single-unit recording, EEG, MEG, ECoG, PET, fMRI
INTERVENE
Directed lesions, TMS, tDCS, implanted stimulation, drugs, optogenetics
DESIGN AND ANALYZE
Task contrasts, dissociations, controlled trials, MVPA, connectivity, computational models, evidence synthesis
MEASURE OUTCOMES
Choices, accuracy, reaction time, symptoms, adverse events, surveys, interviews

## Slide 4
Three questions for every empirical study
METHOD
ANALYSIS
WARRANT
4
METHOD
What produced the data?
ANALYSIS
How did the study turn the data into a result?
WARRANT
What conclusion does the result support?
Warrant pertains to the kind of inference made and the strength of evidence in support of it

## Slide 5
No method dominates every comparison
METHOD
ANALYSIS
WARRANT
5
Method | Signal or intervention | Coverage | Timing | Causal leverage | Main limitation
Single-unit | Spikes from selected neurons | Very narrow | Milliseconds | Observational | Invasive; selective sampling
EEG / MEG | Population electrical / magnetic signal | Broad | Milliseconds | Observational | Source localization is model-dependent
PET activation | Tracer distribution | Whole brain | About a minute | Observational | Radioactivity; poor timing
BOLD fMRI | Neurovascular signal | Whole brain | Seconds | Observational | Indirect; temporally blurred
Lesion comparison | Existing neural damage | Variable | No event timing | Causal contribution | Extent, recovery, network disruption
TMS | Induced cortical activity change | Limited targets | Protocol varies | Causal contribution | Spread; limited depth

## Slide 6
Electrical recording
METHOD
ANALYSIS
WARRANT
6
SINGLE-UNIT
Spikes from selected neurons
EEG
Scalp voltage reflecting summed postsynaptic currents in synchronized populations
ERP
An event-locked response estimated from EEG across repeated trials
MEG
Magnetic fields generated by neural current flow
ECOG
Electrical activity recorded from the cortical surface
MEG sensors
scalp EEG
ECoG
single-unit
event
event-locked average (illustrative)

## Slide 7
Electrical recording setups
METHOD
ANALYSIS
WARRANT
7
EEG
Electrodes on the scalp
MEG
Helmet-shaped magnetic sensors
SINGLE-UNIT
Fine probes sample spikes from selected neurons
ECoG
An electrode grid rests on the cortical surface

## Slide 8
PET and fMRI detect physiology associated with neural activity
METHOD
ANALYSIS
WARRANT
8
PET ACTIVATION IMAGING
BOLD fMRI
Radioactive tracer
Signal accumulates over about a minute
Practical localization around a centimeter in the assigned example
Endogenous MR contrast
Signal is related to blood oxygenation
Several-millimeter localization; response unfolds over seconds

## Slide 9
BOLD is a delayed neurovascular signal
METHOD
ANALYSIS
WARRANT
9
ILLUSTRATIVE HEMODYNAMIC RESPONSE
relative MR signal
0
5
10
15
20
time after event (s)
event
delayed rise
undershoot
1 NEURAL ACTIVITY
Population activity changes local metabolic demand.
2 VASCULAR RESPONSE
Blood flow and oxygen delivery follow the neural event.
3 DEOXYHEMOGLOBIN
Its local concentration changes over the next few seconds.
4 MR SIGNAL
The measured BOLD signal rises and returns toward baseline.
Textbook example: onset ~1–2 s · peak ~5–6 s · return toward baseline ~12–15 s

## Slide 10
Design and contrast turn time series into interpretable results
METHOD
ANALYSIS
WARRANT
10
BLOCK DESIGN
A
A
REST
B
B
Sustained periods of different conditions
EVENT-RELATED DESIGN
A
B
A
A
B
A
B
Responses estimated for individual event types
TASK CONTRAST
Condition A
−
Condition B
=
specified comparison
MODEL + THRESHOLD
thresholded statistical estimates
An activation map is not the scanner’s raw output. It is the result of a specified design, model, contrast, and threshold.

## Slide 11
Reverse inference adds a premise the map does not supply
METHOD
ANALYSIS
WARRANT
11
OBSERVED RESULT
Region R responds differently in Condition A and Condition B.
SUPPORTED CONCLUSION
Activity in Region R is associated with the condition difference.
ADDITIONAL PREMISE
Region R responds selectively to Process P.
REGION R
Process P
Process Q
Process S
Process T
Without evidence of selectivity, Region R does not uniquely identify Process P.

## Slide 12
Damage and perturbation increase causal leverage
METHOD
ANALYSIS
WARRANT
12
DOUBLE DISSOCIATION · ILLUSTRATIVE
Chart: Performance
| Task A | Task B
Lesion group 1 | 25 | 82
Lesion group 2 | 80 | 28
PERTURBATION QUESTION
Change neural activity or signaling
↓
Measure behavior or another outcome
↓
Infer causal contribution—with limits
Selectivity · spread · compensation · task design · outcome measurement

## Slide 13
Representational analyses ask what patterns can discriminate
METHOD
ANALYSIS
WARRANT
13
MVPA
Similar regional means; different voxel patterns
Condition A
Condition B
Can a multivoxel pattern discriminate conditions in held-out data?
REPETITION SUPPRESSION
Under an adaptation model, does repetition reduce the response?
first A
repeat A
new B
Prediction within a study does not guarantee interpretation—or accuracy for a new person.

## Slide 14
Connectivity measures dependence—not causal direction
METHOD
ANALYSIS
WARRANT
14
Functional connectivity measures statistical dependence among signals.
A influences B
B influences A
A third process influences both
A
→
B
B
→
A
C
A
B
The same covariation can fit several causal structures.
Directional models compare specified hypotheses; conclusions depend on the model and design.

## Slide 15
The ethical question determines which outcomes matter
METHOD
ANALYSIS
WARRANT
15
PERSON
BEHAVIOR
Choice, accuracy, reaction time
CLINICAL OUTCOMES
Symptoms, functioning, adverse events, follow-up
FIRST-PERSON EVIDENCE
Surveys, interviews, qualitative analysis
EVIDENCE SYNTHESIS
Systematic review across studies
NEURAL EVIDENCE
Recorded signals and perturbation effects
What did the person do? Did an intervention help or harm? How did participants understand the experience? How consistent is the literature?

## Slide 16
Designing a moral-judgment study
METHOD
ANALYSIS
WARRANT
16
People often judge switching a trolley differently from pushing a person, even when both actions could save five people at the cost of one life.
SWITCH
trolley
FOOTBRIDGE
trolley
METHOD
What behavioral or neural signals would you record?
ANALYSIS
What conditions would you compare? What baseline would make the comparison meaningful?
WARRANT
What could a difference between conditions support? What would remain unresolved?
Pairs: choose measures · specify a comparison and baseline · state one warranted conclusion and one limit

## Slide 17
NEXT: THE FIELD AND THE ETHICAL TOOLKIT
What combination of evidence
would justify the claim?
RECORD
covariation
PERTURB
causal contribution
BEHAVIOR + EXPERIENCE
consequences for persons
NORMATIVE PREMISES
ethical conclusion
Convergence is strongest when methods have different limitations—and every conclusion still depends on design, analysis, and assumptions.
METHOD
ANALYSIS
WARRANT
17